## Slide 1
DriftLock
We don't match images — we invert the microscope.
Cross-magnification pattern localization in repetitive semiconductor layouts. Because the forward model of the acquisition is known, localization is an inverse problem rather than a similarity search — and the periodic lattice everyone treats as the enemy turns out to be the most precise ruler in the image.
23.3%
mis-lock, held-out bench
0.254 px
median error, located pairs
63.3%
sub-pixel pass rate
one cell in ten thousand looks like every other
Team DriftLock · SEMICON India Hackathon 2026 · Applied Materials “Drift-Sense”
Notes: DriftLock locates a 100x reference pattern inside a 10x search image. The thesis: we know the forward model, so localization is a maximum-likelihood inverse problem, not a similarity search.

## Slide 2
The problem, and why it is genuinely hard
A wrong answer does not look wrong — it looks like a perfect match one cell over
Cross-magnification localization
• Reference: 1000 × 1000 at 100× (1 nm per pixel)
• Search: 1000 × 1000 at 10× (about 10 nm per pixel)
• So the reference occupies only 100 × 100 px of the search image — 1% of its area
Why periodicity is the whole problem
A DRAM array is periodic by design, so a wrong repeat is a structurally valid match — not a blurry one that a better similarity measure would reject. Measured on real pairs, the true location beats its best impostor by a median of only 0.016 in correlation while sitting 45 px away.
What a mis-lock costs downstream
1
The tool moves to the wrong cell
it then measures a structurally identical but different site
2
The error is invisible to averages
a mis-lock is off by tens to hundreds of px; a good match by about one
3
So mis-lock rate is reported separately
a single mean error would hide the failure mode entirely
The bar we had to beat
The published baseline resizes over five fixed scales, takes the correlation argmax and adds half the template size. It has no sub-pixel step, so its answer is always an integer plus 50.0 — a hard quantization floor it cannot score below.
25.0% mis-lock · 1.102 px median
Notes: The mis-lock rate is reported separately because the error distribution is bimodal - a pair is either located to about a pixel, or lost by hundreds.

## Slide 3
End-to-end workflow
Every stage exists because a measurement demanded it — none is generic vision hygiene
1
Measure the pose
A coarse pyramid search recovers magnification and rotation. Measured where it is cheap, not searched at full resolution.
2
Invert the acquisition
Box-integrate the reference over the detector footprint, then one affine carrying scale and rotation — the exact forward operator.
3
Correlate, keep candidates
ZNCC across the pose bracket; the nominal 10:1 hypothesis is always retained as a fallback.
4
Refine to sub-pixel
Upsampled-DFT cross-correlation (Guizar-Sicairos et al., 2008).
5
Cancel the raster drift
Two-axis measurement: drift is anisotropic and rotation is isotropic, so the tilt cancels exactly.
6
Emit coordinate + confidence
Sub-pixel centre in search pixels, plus an ambiguity index saying how much to trust it.
Deterministic, CPU-only, four runtime dependencies. No GPU, no learned weights, no network access at run time.

## Slide 4
Synthetic dataset design
Our own generator — because the published one cannot produce the envelope the spec says will be tested
Structure — public knowledge only
• DRAM 6F² folded-bitline arrays, with FinFET as the second architecture
• Contacts on an (i+j)%2 checkerboard, so the dangerous confusion is the parity-preserving diagonal shift
• Mats separated by peripheral routing strips, each mat drawn independently
The detail that makes localization possible at all
Line positions are laid down as a random walk rather than on an exact grid — real line-edge roughness. That accumulated deviation is the only thing distinguishing one cell from its neighbour. A perfectly periodic array would be impossible to localize within, by anyone.
What ours does that the published generator does not
Rotation and scale
±2° and 9:1–11:1 — the envelope the spec says will be tested
SE edge brightening
theirs paints flat grey levels per material
Continuous ground truth
fractional crop origins, not a 0.1 px grid
Per-mat geometry
in theirs, every DRAM preset renders identically
Reproducible from seeds rather than shipped as blobs: the same seed regenerates byte-identical images, and every pair carries its full parameter set in the manifest.

## Slide 5
Degradation modelling, in physically correct order
Noise before blur, or edge contrast after the beam PSF, looks plausible to a vision engineer and obviously wrong to a microscopist
layout
SE edge yield
charging
beam PSF
rotation + scale
raster drift
shot noise
detector noise
quantise
Literature basis — every row opened and verified, not cited from memory
Secondary-electron yield vs. surface tilt
Villarrubia, Ritchie & Lowney, Proc. SPIE 6518, 65180K (2007)
the edge-brightening term the starter omits
Poisson–Gaussian noise, variance stabilisation
Mäkitalo & Foi, IEEE TIP 22(1):91–103 (2013)
why correlation is not automatically maximum-likelihood
Sub-pixel registration by upsampled DFT
Guizar-Sicairos, Thurman & Fienup, Optics Letters 33(2) (2008)
our refinement stage
Rotation and scale via log-polar spectra
Reddy & Chatterji, IEEE TIP 5(8) (1996)
implemented, measured, and rejected on evidence
6F² DRAM folded-digitline architecture
US Patent 7,349,232 B2
public structural basis for the layout
Closest-to-origin rule for periodic patterns
Hitachi High-Tech, US Patent 7,925,095 B2
the spec's tie-break is established industry practice
Notes: Rule R1: a citation nobody opened is not a citation. REFERENCES.md records who verified each row and on what date.

## Slide 6
Localization method and decision rule
Three ideas do the work
1
The forward operator is the physics, not a resize
The search image is formed by integrating over the detector footprint and sampling through an affine, so we build the template with exactly that operator. The previous resize could only emit integer template sizes, quantising magnification to about 1% steps — as coarse as the entire tolerance. No pose search could ever have worked.
2
Pose is measured on a pyramid, not searched at full resolution
Scale error costs misalignment proportional to template size, so downsampling four times widens the usable basin from about 1% to about 4%. The whole 9:1–11:1 envelope becomes roughly eleven cheap hypotheses instead of hundreds of expensive ones.
3
Drift is anisotropic; rotation is isotropic
A tilted field of view and a drifting raster produce the same row-to-row displacement, so one measurement cannot separate them. Repeating it on the transposed image isolates the tilt, and the two subtract exactly — no rotation estimate, no tuned parameter.
The decision rule
“If several valid matches exist, select the one whose centre is closest to the search-image centre.”
Implemented, tested, and reachable — but off by default, and the reason is the interesting part.
The rule encodes a DEPLOYMENT PRIOR: a tool that has drifted lands near the site it meant to revisit, so among equally-scoring candidates the central one is the likely one.
Both benchmarks place targets uniformly. Measured median distance from the search centre is 373 / 335 / 347 px against the 358 px a uniform draw predicts — the prior is absent, so the rule can only lose here.
We also fixed its threshold: a tie is now two standard errors of the correlation, not a fraction of the candidate spread.
Refinement fails gracefully; re-ranking fails destructively — so only strictly-additive stages ship by default.

## Slide 7
Implementation and execution
The evaluator must be able to run this on their own data with zero source edits
# single pair — prints exactly one line: "547.03,289.62"
python localize.py --reference ref.png --search search.png
# batch — a manifest or a directory of pairs
python localize.py --manifest test/manifest.csv --out pred.csv
python localize.py --input-dir data/test/ --out pred.csv
# regenerate the dataset, then score it
python generate_dataset.py --num-samples 30 --split bench --seed 1234
python evaluate.py --manifest m.csv --predictions pred.csv --out results/
Four runtime dependencies
numpy, scipy, opencv-python-headless, scikit-image. torch is optional and lazily imported — uninstalling it changes nothing.
Deterministic and portable
One seeded RNG threaded through, pathlib only, no absolute paths. Timing method and thread count are recorded with every run (OpenCV using 22 threads here). Developed on macOS and re-measured on Windows for this submission; accuracy reproduced to the digit on both.
stdout discipline
In single-pair mode stdout carries the coordinate and nothing else. All logs go to stderr, because benchmark parsers break on chatty scripts.
Repository layout
src/synth/ dataset generation src/driftlock/ localization localize.py inference CLI generate_dataset.py evaluate.py metrics + strata results/ every number here docs/ plan, decisions, findings, worklog tests/ 35 tests, asymmetric geometry cases
Correctness discipline
No number is typed by hand — every metric in this deck is read out of results/ at build time, and a verifier fails the build on any slide number that is not there. No citation nobody opened. Asymmetric geometry tests, because a symmetric test cannot catch an x/y swap.

## Slide 8
Experiment setup and test diversity
Three splits, only one of which was ever used to make a decision
sponsor · 40 pairs
The published generator — an independent distribution we did not author. Fixed 10:1, no rotation. Tests precision.
bench · 30 pairs
Our generator: 9:1–11:1 magnification, ±2° rotation, DRAM. Never used for tuning. The reported split.
held-out FinFET · 30 pairs
A different architecture entirely, different seed. Never used for tuning. Tests whether anything transfers.
Held-out discipline, and why we enforce it
An earlier component improved the split it was tuned on by 5 points and made both held-out splits worse — by 6.7 points on one and 13.3 on the other. It had been tuned on a single seed and a single architecture. It was withdrawn, and the headline that depended on it was withdrawn with it. That is why every claim here is quoted on a split that was never used to make a decision.
What varies across the pairs
• Magnification 9:1 to 11:1, continuously sampled
• Rotation ±2°, continuously sampled
• Target position uniform across the field, plus a deliberate share on mat boundaries
• Dose 2000 on the reference against 200 on the search — a ten-times noisier acquisition
• Two architectures, four presets each, per-pair seeds recorded

## Slide 9
Threshold-wise accuracy, error statistics and runtime
Every figure emitted by evaluate.py into results/ — none typed by hand
Split | Config | Mis-lock | Median | @5px | @2px | @1px | @0.5px | Runtime p50
sponsor | baseline | 25.0% | 1.102 | 75.0% | 75.0% | 40.0% | 17.5% | 64 ms
sponsor | DriftLock | 25.0% | 0.297 | 75.0% | 75.0% | 72.5% | 67.5% | 1228 ms
bench | baseline | 76.7% | 326.905 | 23.3% | 23.3% | 10.0% | 3.3% | 32 ms
bench | DriftLock | 23.3% | 0.343 | 76.7% | 73.3% | 73.3% | 63.3% | 1190 ms
FinFET | baseline | 90.0% | 359.893 | 10.0% | 6.7% | 3.3% | 3.3% | 32 ms
FinFET | DriftLock | 16.7% | 0.313 | 83.3% | 83.3% | 80.0% | 63.3% | 354 ms
Reading the table
On the sponsor's fixed 10:1 data the task is precision: median error improves from 1.102 px to 0.297 px and the sub-pixel pass rate rises from 17.5% to 67.5%. On our own data — the 9:1–11:1 and ±2° envelope the problem statement says will be tested — the baseline does not work at all (76.7% mis-lock against 23.3%). That axis is invisible to anyone validating only on the published generator, because it produces neither rotation nor scale variation.
Chart: Mis-lock rate (%) — lower is better
| sponsor | bench | FinFET
Baseline | 25 | 76.6667 | 90
DriftLock | 25 | 23.3333 | 16.6667
Windows 11 (AMD64) · Intel64 Family 6 Model 170 Stepping 4, Genui · Python 3.14.3 · OpenCV 5.0.0 · time.perf_counter() around load+localize, per pair, OpenCV using 22 thread(s), no warm-up discarded

## Slide 10
Ablation and robustness — including everything that failed
A method we tried and dropped with its measurement attached is evidence; a silently omitted experiment is cherry-picking
Stage | sponsor | bench | FinFET | Verdict
Baseline: resize + ZNCC argmax | 25.0% | 76.7% | 90.0% | the floor
+ sub-pixel DFT | 25.0% | 76.7% | 90.0% | precision only
+ two-axis drift cancellation | 25.0% | 76.7% | 90.0% | precision only
+ pose: pyramid ← shipped | 27.5% | 26.7% | 33.3% | solves rotation/scale
+ per-candidate pose refit ← shipped | 25.0% | 23.3% | 16.7% | solves selection
+ spec's centre rule | 35.0% | 20.0% | 20.0% | prior absent
+ pose: spectral lattice | 22.5% | 46.7% | 60.0% | less accurate
+ PADM residual re-ranking | 27.5% | 70.0% | 73.3% | overfit
+ max-likelihood re-ranking | 22.5% | 36.7% | 50.0% | no gain
+ coarse-level consensus | 62.5% | 73.3% | 36.7% | harmful
+ row destriping | 35.0% | 90.0% | 90.0% | harmful
Mis-lock rate. Rows are baseline plus the named stage, not a cumulative chain.
Four attempts at selection, and why the fourth worked
PADM residual scoring — overfit
Two tuned constants. Gained on the split it was tuned on, lost on both held-out splits.
Coarse consensus — harmful
Assumed downsampling reveals landmarks. It cannot: the reference's footprint is smaller than a mat, so there is nothing to reveal at any resolution.
Maximum-likelihood — no gain
The noise really is signal-dependent, so ZNCC really is mis-weighted. But model mismatch is larger than photon noise, so weighting by photon variance sharpens the wrong term.
Per-candidate pose refit — WORKS
Follows the line above: if mismatch dominates, reduce mismatch. Each candidate is re-SCORED at its own best pose — no new criterion, so it cannot invent a preference.
Two rules these bought. Downsampling is free for measuring pose and ruinous for deciding identity — pose is a global low-frequency property, identity lives only in the full-resolution aperiodic fingerprint. And refinement fails gracefully while re-ranking fails destructively, so a selection stage must remove a handicap rather than introduce a criterion.

## Slide 11
Failure analysis — the worst pair, and what it proves
Not a picture of a wrong answer: a measurement of why it was wrong
Worst case on the reported split
• Euclidean error 893.89 px — a different site entirely
• The true location WAS a candidate, at rank 4
• It lost by 0.0027 of correlation — 0.32% of the winning score
• The pair sits in the 'med' ambiguity stratum — no landmark in view
Root cause: ranking, not candidate generation.
Failures concentrate exactly where theory says they must
Our generator labels each pair by whether an aperiodic landmark is in view. Stratifying the results by that label:
Crop contains | n | Mis-lock | @1px
a mat boundary | 21 | 10% | 90%
only lattice | 9 | 56% | 33%
5 of the 7 failures fall in those 9 pairs. The method fails precisely where the information needed to succeed is absent — the honest definition of the problem's limit.
Limitations, stated rather than left to be found
Selection is still the cap
Every pass rate is capped by the mis-lock rate. The truth is in the top-20 on 28/30 pairs (93.3%), so a perfect re-ranker would still have room to roughly halve what remains.
Runtime above our own target
About 1190 ms per pair against a 300 ms goal. The per-candidate refit is most of it; top_k is the dial. We took 9 points of mis-lock for the time.
Untested axes remain
Barrel distortion, astigmatism, charging streaks and impulse noise are modelled but not stratified — untested, not proven harmless.

## Slide 12
What we built, and what we learned
76.7% → 23.3%
Mis-lock, held-out DRAM bench
90.0% → 16.7%
Mis-lock, held-out FinFET
17.5% → 67.5%
Sub-pixel rate, sponsor data
The three findings we would carry to any similar problem
1
Own the generator, or you cannot see your own blind spots.
Two bugs were structurally invisible in the published data — a half-pixel ground-truth convention, and a drift estimator that silently mistook rotation for drift. Neither could ever have surfaced on a generator that produces no rotation.
2
Ask what makes two effects physically different, not how to estimate one better.
Drift and rotation were inseparable by any single measurement, and subtracting an estimate made things worse than doing nothing. Measuring both axes made the tilt cancel exactly, with no parameter to tune.
3
The elegant method has to win on measurement like everything else.
Reading magnification off the lattice is the idea this project is named for. It lost to a coarse pyramid search, because a 1000 nm reference spans as few as four lattice periods — a fine ruler, but a short one.
Next: the correct answer is still in the candidate set on 28/30 pairs, so selection remains the cap — and the one stage that beat it did so by removing a handicap, not by scoring harder.
Notes: Everything in results/ is regenerated by `make bench`; scripts/verify_submission.py fails the build on any deck number not found there.